## Slide 1: Beyond Throughput, The Next Generation: A 5G Dataset with Channel and Context Metrics
Darijo Raca, Dylan Leahy, Cormac J. Sreenan,
Jason J. Quinlan
This publication has emanated from research conducted with the financial support of Science Foundation Ireland (SFI) under Grant Number 13/IA/1892 and European Regional Development Fund under SFI Grant 13/RC/2077
Notes: Hi. My name is Darijo and today I will present a joint work by University College Cork and Faculty of Electrical Engineering Sarajevo by the name “Beyond Throughput, the next generation: a 5G Dataset with channel and context metrics
This work is supported by Science Foundation Ireland and European Regional Development Fund.

## Slide 2
Current Trends
Rapid increase in the number of connected device - over 75 billons by the 2025
Rise in multimedia traffic – video on demand, live streaming and 360-degree video
Requirements:
High bandwidth
Low latency
Notes: If we look at current trends, we can observe that there are currently billion connected devices in the world. It is estimated that these number will reach 75 billions by the 2025. It goes without saying that these devices are connected through the wireless channel putting a high requirements on the mobile communication systems.
Along this, there is a huge growth in multimedia traffic, ranging from video on demand, live streaming and 360-degree video.
This brings us to our final point, that in order to support these services and applications, mobile communication systems needs to provide high bandwidth and low latency

## Slide 3
Promise of 5G
High data rates ~ 1Gbps
Low latency ~ 1ms
Support for tens of thousands devices
Can current 5G deployments support these claims?
Notes: This brings us to fifth generation cellular network or simply 5G. 5G promise just that, high rates and low latency
Rates go up to 1Gbps with latency around 1ms. While these numbers can seem as good enough, let’s put it into the perspective.
For example, a 24K 360-degree video with 120 frame-per-second can consume several Gbps. Also, as user can change field of-view, and in order not to experience motion sickness, latency during the transition needs to be less than 20ms.
Also, 5G provides connectivity for tens of thousands of devices in order to support future Internet of Things (IoT) and Internet of Vehicle (IoV) paradigms.
However, we ask ourselfs, in practice, can current 5G deployments support these claims?
This neatly brings us to our work

## Slide 4
Production 5G dataset
Dataset collected from the Irish mobile operator’s 5G network
Two mobility patterns: static and driving
Different download patterns: file download and VoD streaming services
Supplemented with synthetic dataset generated from large-scale mmwave ns-3 framework
Notes: We present a production 5G dataset
Our dataset is collected in a production mobile operators 5g network, capturing throughput, latency and channel conditions
Dataset is collected over a few months with two mobility patterns: static (mostly indoor) and driving (mostly commute routes)
We used two different download patterns, file download and streaming using popular VoD services.
Finally, we supplements our production dataset with synthetic dataset generated from the large scale 5G ns-3 simulation

## Slide 5
Dataset collection
Measurement application: G-NetTrack
Mobile device: Samsung S10 5G
Sampling interval: 1 second
Test applications:
                - file download (200MB file)
                - Netflix
                - Amazon Prime
Traces are collected over period of several months

## Slide 6
Dataset features
Throughput: uplink and downlink
Latency
Channel metrics: SNR, RSRQ, RSRP, RSSI, CQI
Context metrics: GPS coordinates, velocity, state (idle/active)

## Slide 7
Dataset overview
4G vs. 5G
5G improves average throughput by up to 50%
Peak rate: 532Mbps
Notes: Next we compare 5G dataset with our previously collected 4G dataset. To offer a fair comparison, we only compare traces from the same mobile operator and with the same mobility patterns.
As expected, 5G allows higher rates, with a up to 50% increase for the average throughput in the case for the static scenario. However, for the driving scenario, the average throughput increased only by 27% for 5G compared to 4G. The
main reason for “minor” improvement is lack of 5G base stations across all driving routes, forcing the device to use 4G.

## Slide 8
Dataset overview
VoD consumes significantly less bandwidth
(ON-OFF behavior)
File download vs. streaming
Notes: Next, we compare performance between different application types. Intuitively, continuous file download has the highest average throughput as shown in table.
Also we can look at the relationship between CQI and application throughput as shown in the figure. Figure shows the range of throughput values for each CQI
separately. Overall, we observe an increasing trend in throughput proportional to CQI. However, the range of throughput values oscillates significantly for each CQI.
For Amazon Prime, lower bitrates result in similar throughput rates across all CQI values. Streaming services download segments only during the ON phase (buffer filling). Also, bandwidth demand is limited by the maximum quality of encoded video content. Overall, Netflix consumes significantly more bandwidth than Amazon Prime for both mobility patterns, as a result of the higher encoding quality and thus larger segment sizes.

## Slide 9
Simulation Framework
Dataset mimics features of production dataset
Large scale
  - up to 20 eNB
    - up to 20 users per eNB
Allows capturing network-side metrics

## Slide 10
Datasets use cases
Multi dimensional aspects of datasets allow for various use cases:

## Slide 11
Conclusion
5G production dataset consisting of client-side metrics
Captures throughput and channel measurements from the real network
Simulation 5G framework
Allows large-scale multi-cell evaluation

## Slide 12
Darijo Raca
E-mail: draca@etf.unsa.ba
Jason Quinlan
E-mail: j.quinlan@cs.ucc.ie
Cormac Sreenan
E-mail: cjs@cs.ucc.ie